Education with QtRVSim – RISC-V Simulator
Education with QtRVSim – RISC-V Simulator
Základní princip činnosti procesoru a jeho výuka s RISC-V simulátorem QtRVSim
InstallFest 2022
Czech Technical University in Prague
More information:	https://comparch.edu.cvut.cz/
QtRVSim	https://github.com/cvut/qtrvsim
Karel Kočí <cynerd@email.cz>
Jakub Dupák <dupakjak@fel.cvut.cz>
Pavel Píša <pisa@fel.cvut.cz>
Michal Štepanovský <michal.stepanovsky@gmail.com>

---
QtRVSim – RISC-V Computer Architecture Simulator
QtRVSim – RISC-V Computer Architecture Simulator
Run
Single Step
Load
Make
Exceptions
control
Registers
Terminal
Assembler
Editor
Peripherals
Data memory
CPU core view
single cycle
pipelined
Code
Cache

---
QtRVSim – Download
QtRVSim – Download
- Project Sources
  https://github.com/cvut/qtrvsim
- Windows, Linux, Mac
  https://github.com/cvut/qtrvsim/releases
- Ubuntu
  https://launchpad.net/~qtrvsimteam/+archive/ubuntu/ppa
- Suse, Fedora and Debian
  https://software.opensuse.org/download.html?project=home%3Ajdupak&package=qtrvsim
- Online version
  https://comparch.edu.cvut.cz/qtrvsim/app

---
QtRVSim – Origin and Development
QtRVSim – Origin and Development
- MipsIt used in past for Computer Architecture course at the Czech Technical University in Prague, Faculty of Electrical Engineering
- Switch to QtMips in the 2019 summer semester
  - Result of diploma theses of Karel Kočí
    Graphical CPU Simulator with Cache Visualization
    https://dspace.cvut.cz/bitstream/handle/10467/76764/F3-DP-2018-Koci-Karel-diploma.pdf
- Switch QtRVSim in the 2022 summer semester
  - Graphical RISC-V Architecture Simulator - Memory Model and Project Management
    Jakub Dupák; 2021; Bachelor Thesis
    https://dspace.cvut.cz/bitstream/handle/10467/94446/F3-BP-2021-Dupak-Jakub-thesis.pdf
  - Graphical RISC-V Architecture Simulator - Instructions Decode and Execution and OS Emulation
    Max Hollmann; 2021; Bachelor Thesis
    https://dspace.cvut.cz/bitstream/handle/10467/96707/F3-BP-2021-Hollmann-Max-thesis.pdf

---
MIPS and RISC-V Education Simulator Alternatives
MIPS and RISC-V Education Simulator Alternatives
- SPIM/QtSPIM: A MIPS32 Simulator
  http://spimsimulator.sourceforge.net/
- MARS: IDE with detailed help and hints
  http://courses.missouristate.edu/KenVollmar/MARS/index.htm
- EduMIPS64: 1x fixed and 3x FP pipelines
  https://www.edumips.org/
- RARS – RISC-V Assembler and Runtime Simulator
  https://github.com/TheThirdOne/rars
- RIPES – A graphical processor simulator and assembly editor for the RISC-V ISA
  https://github.com/mortbopet/Ripes/

---
The main instruction cycle of the CPU
The main instruction cycle of the CPU
1. Initial setup/reset – set initial PC value, PSW, etc.
2. Read the instruction from the memory
  - PC → to the address bus
  - Read the memory contents (machine instruction) and transfer it to the IR
  - PC+l → PC, where l is length of the instruction
1. Decode operation code (opcode)
2. Execute the operation
  - compute effective address, select registers, read operands, pass them through ALU and store result
1. Check for exceptions/interrupts (and service them)
2. Repeat from the step 2

---
C → Assembler → Machine Code
Compilation: C → Assembler → Machine Code
/* ffs as log2(x)*/
int x = 157;
1. int y = 0;
  while(x != 0)
  {
  x = x / 2;
  y = y + 1;
  }
_start:	addi	a0, zero, 157	// int x = 157;
addi	t1, zero, -1	// int y = 0;
beq	a0, zero, done	// while(x != 0) {
loop:	srli	a0, a0, 1	// x = x / 2;
addi	t1, t1, 1	// y = y + 1;
bne	a0, zero, loop	//}
done:	addi	a0, t1, 0
finish:	ebreak
beq	zero, zero, finish
0x00000200	09d00513	addi x10, x0, 157
0x00000204	fff00313	addi x6, x0, -1
0x00000208	00050863	beq x10, x0, 0x218
0x0000020c	00155513	srli x10, x10, 0x1
0x00000210	00130313	addi x6, x6, 1
0x00000214	fe051ce3	bne x10, x0, 0x20c
0x00000218	00030513	addi x10, x6, 0
0x0000021c	00100073	ebreak
https://gitlab.fel.cvut.cz/b35apo/stud-support/
seminaries/qtrvsim/ffs-as-log2

---
Instruction Encoding Constrains
Instruction Encoding Constrains
Instruction
- Encode 256 combinations in 8-bits
- Opcode and address to directly operate on megabytes of ram does not fit
- Use some limited number of fast accessible registers or use stack concept
- 8 registers, 3 bits to encode, for two operand operations (a += b, mem[a] = b), 6 bits to select registers→only 4 operations in total
- 16 bit (65536), 16 registers, 256 two operands or 16 three operands (4 + 3 * 4 bits)
- 32 bit, 32 registers, three operands (17 + 3 * 5)
- But immediate for arithmetic and address usually required (CISC followup words, RISC uses limited ranges and some other mechanism)
bits
8
16
32
reserve part of code space for longer operations

---
RISC-V – Instruction Length Encoding
RISC-V – Instruction Length Encoding

---
RISC-V Processor Registers
RISC-V Processor Registers
Register	ABI Name	Description	Saver
x0	zero	Hard-wired zero
x1	ra	Return address	Caller
x2	sp	Stack pointer	Callee
x3	gp	Global pointer	–
x4	tp	Thread pointer	–
x5	t0	Temporary/alternate link register	Caller
x6–7	t1– 2	Temporaries	Caller
x8	s0/fp	Saved register/frame pointer	Callee
x9	s1	Saved register	Callee
x10–11	a0–1	Function arguments/return values	Caller
x12–17	a2–7	Function arguments	Caller
x18–27	s2–11	Saved registers	Callee
x28–31	t3–6	Temporaries	Caller
pc	pc	Program Counter
f0–31		Floating point
		Machine control and status

---
Hardware realization of basic (main) CPU cycle
Hardware Realization of Basic (main) CPU Cycle
Program counter, 32 b
Instruction memory
instruction, 32 bits
constant 4
Instruction address
Next instruction address

---
Design of the Single Cycle CPU
- To understand the implementation of a simple computer consisting of CPU and separated instruction and data memory
- Our goal is to implement following instructions:
  - Read and write a value from/to the data memory
    lw – load word, sw – store word
  - Arithmetic and logic instructions: add, sub, and, or, slt
    Immediate variants: addi,ori, upper bits loads olui,auipc
  - Program flow change/jump instruction beq
  - Subroutine call jal, jalr (provides even return from subroutine jr ra)
- CPU will consist of control unit and ALU (data path).
- Notes:
  - The implementation will be minimal (single cycle CPU – all operations processed in the single step/clock period)
  - The lecture 5 focuses on more realistic pipelined CPU implementation

---
Subset of RISC-V Instructions to Implement
Subset of RISC-V Instructions to Implement
Instruction	Executed operation
lw rd, imm12(rs1)	[rd] ← Mem[[rs1] + imm12];
sw rs2, imm12(rs1)	Mem[[rs1] + imm12] ← [rs2];
addi rd, rs1, imm12	[rd] ← [rs1] + imm12;
add rd, rs1, rs2	[rd] ← [rs1] + [rs2];
sub rd, rs1, rs2	[rd] ← [rs1] – [rs2];
and rd, rs1, rs2	[rd] ← [rs1] & [rs2];
or rd, rs1, rs2	[rd] ← [rs1] | [rs2];
slt rd, rs1, rs2	[rd] ← [rs1] < [rs2];
beq rs1, rs2, imm12	if [rs1] == [rs2] go to [PC]+(imm12<<1); else go to [PC]+4;
jal rd, imm20	[rd] ← [PC]+4; go to [PC]+(imm20<<1);
jalr rd, rs1, imm12	[rd] ← [PC]+4; go to [rs1]+imm12;
lui rd, imm20	[rd] ← imm20<<12
auipc rd, imm20	[rd] ← PC+(imm20<<12)
Remark, all immediate operands are signed

---
The RISC-V Instruction Format and Instruction Types
The RISC-V Instruction Format and Instruction Types
The six basic formats of the instructions are considered:
- opcode – specify operation, func 3 and func 7 variant
- rs1 – source 1, rs2 – source 2, rd – destination
- 5 bits allows to encode 32 GPRs ($0 is hardwired to 0/discard)

---
RISC-V Immediate Operand Encoding
RISC-V Immediate Operand Encoding
There are five options how to form immediate operand
- goal: keep same position in the instruction for corresponding bit (compare U and J, B and S, S and I)
- sign in instruction bit 31 (needs fan-out to drive multiple bits)

---
Opcode encoding
Opcode encoding
The primary selection of operation is opcode
Opcode	The group, operation	Actual operations for our subset
0110011	R-type (see funct7 and funct3)	add, sub, slt, or, and
0010011	ALU-imm (see funct3)	addi
0000011	Memory load (funct3 = 010)	lw
0100011	Memory store (funct3)	sw
1100011	Branch (see funct3)	beq
1101111	jal	jal
1100111	jalr	jalr
0000111	lui	lui
func7	fun3	instruction/ALU operation
0000000	000	add
0100000	000	sub
0000000	010	slt
0000000	110	or
0000000	111	and

---
CPU Building Blocks
CPU Building Blocks
Write at the rising edge of CLK when WE = 1
Multiplexer
Read after “enough time” for data propagation
Instr. Memory
(ROM)
A RD
32
32
PC’
PC
32
32
CLK
5
Reg.
File
A1
A2
A3
WE3
RD1
RD2
WD3
5
5
32
32
CLK
32
Data Memory
A RD
WD
WE
32
32
32
CLK

---
The Load Word Instruction
The Load Word Instruction
lw – load word – load word from data memory into a register
Description	A word is loaded into a register from the specified address
Operation:	[rd] ← Mem[[rs1] + imm12];
Syntax:	lw rd, imm12(rs1)
Encoding:	iiii iiii iiii ssss s010 dddd d000 0011
Example: Read word from memory address 0x400 into register number 2:
lw x2, 0x400(x0)
iiii iiii iiii ssss s010 dddd d000 0011
0100 0000 0000 0000 0010 0001 0000 0011
func3
0x400
0
2
opcode = 3
0x 40 00 21 03 – machine code for instruction lw x2, 0x400(x0)
Note: Register x0 is hardwired to the zero

---
Implementation of the load instruction
Implementation of the load instruction
lw: rs1 – base address, imm12 – offset, rd – register where to store fetched data
I	imm(12), 31:20	rs1(5), 19:15	func3, 14:12	rd(5), 11:7	opcode(7), 6:0
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
ALU
AluOut
SrcB
ReadData
11:7
31:20
Imm decode
SignImm
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3

---
Implementation of the load instruction 2
Implementation of the load instruction
lw: rs1 – base address, imm12 – offset, rd – register where to store fetched data
I	imm(12), 31:20	rs1(5), 19:15	func3, 14:12	rd(5), 11:7	opcode(7), 6:0
Write at the rising edge of the clock
RegWrite = 1
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
ALU
AluOut
SrcB
ReadData
11:7
31:20
Imm decode
SignImm
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3

---
Implementation of the load instruction – PC += 4
Implementation of the load instruction – PC += 4
lw: rs1 – base address, imm12 – offset, rd – register where to store fetched data
I	imm(12), 31:20	rs1(5), 19:15	func3, 14:12	rd(5), 11:7	opcode(7), 6:0
RegWrite = 1
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
ALU
AluOut
SrcB
ReadData
11:7
+
31:20
Imm decode
4
SignImm
PCPlus4
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3

---
The Store Word Instruction
The Store Word Instruction
sw – store word – store word in a register to data memory
Description	Stores a value in register rs2 to given address in memory.
Operation:	Mem[[rs1] + imm12] = [rs2]
Syntax:	sw rs2,imm12(rs1)
Encoding:	iiii iiit tttt ssss s010 iiii i000 0011
Example: Store word in register 2 to memory address computed as addition of value in register 5 and constant 0x404, bit symbol t used for rs2:
sw x2, 0x404(x5)
iiii iiit tttt ssss s010 iiii i000 0011
0100 0000 0010 0010 1010 0010 0010 0011
func3
0x40_
2
5
0x_04
opcode = 35
0x 40 22 a2 23 – machine code for instruction sw x2, 0x404(x5)

---
The Store Word Instruction 2
The Store Word Instruction
sw: rs1 – base address, imm12 – offset, rs2 – select register to store into memory
S	imm(12), 31:25, 11:7	rs2(5), 24:20	rs1(5), 19:15	func3, 14:12	opcode(7), 6:0
MemWrite = 1
RegWrite = 0
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
ALU
24:20
AluOut
SrcB
ReadData
11:7
WriteData
31:25, 24:20
11:7
+
Imm decode
4
SignImm
PCPlus4
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3

---
Instruction for Two Registers Addition
Instruction for Two Registers Addition
add – addition – add content of two registers and store it to destination one
Description	Add together values in two registers (rs1 + rs2) and stores the result in register rd.
Operation:	[rd] = [rs1] + [rs2]
Syntax:	add rd, rs1, rs2
Encoding:	0000 000t tttt ssss s010 dddd d000 0011
Example: Add values in registers 1 and 2 and store result into register 3:
add x4, x2, x3
0000 000t tttt ssss s010 dddd d000 0011
0000 0000 0011 0001 0010 0010 0011 0011
3
2
4
0x 00 31 02 33 – machine code for instruction add x4, x2, x3

---
Instruction for Two Registers Addition 2
Instruction for Two Registers Addition
add: type R, rs, rt – source, rd – destination, funct – select ALU operation = add
R	func(7),31:25	rs2(5),24:20	rs1(5),19:15	func3, 14:12	rd(5),11:7	opcode(7), 6:0
ALUSrc = 0
MemToReg = 0
RegWrite = 1
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
11:7
WriteData
31:25, 24:20
11:7
+
Imm decode
4
SignImm
PCPlus4
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1

---
Single cycle CPU – sub, and, or, slt
Single cycle CPU – sub, and, or, slt
Only difference is another ALU operation selection (ALUcontrol). The data path is the same as for add instruction
ALUSrc = 0
MemToReg = 0
RegWrite = 1
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
11:7
WriteData
31:25, 24:20
11:7
+
Imm decode
4
SignImm
PCPlus4
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1

---
Single cycle CPU – addi, ori, andi
Single cycle CPU – addi, ori, andi
addi – add immediate; [rd] = [rs1] + imm12
I	imm(12), 31:20	rs1(5), 15:19	func3, 14:12	rd(5), 7:11	opcode(7), 6:0
addi rd, rs, imm12
ALUSrc = 1
MemToReg = 0
RegWrite = 1
ALUControl
SrcA
Zero
19:15
Instr
PC
PC’
Result
ALU
24:20
AluOut
SrcB
ReadData
11:7
WriteData
31:25, 24:20
11:7
+
Imm decode
4
SignImm
PCPlus4
ori, andi instructions do not sign extend the immediate operand
Instr. Memory
A RD
Data Memory
A RD
WD
WE
Reg.
File
A1 RD1
A2 RD2
A3
WD3
WE3
0
1
0
1

---
QtRVSim – Simple I/O Peripherals
base of SPILED port region
SPILED_REG_BASE 0xffffc100
RGB LED 1 color components – 8 bits each
SPILED_REG_LED_RGB1 0xffffc110
SPILED_REG_LED_RGB1_o 0x0010
RGB LED 2 color components – 8 bits each
SPILED_REG_LED_RGB2 0xffffc114
SPILED_REG_LED_RGB2_o 0x0014
Three 8 bit knob values
SPILED_REG_KNOBS_8BIT 0xffffc124
SPILED_REG_KNOBS_8BIT_o 0x0024
line of 32 LEDs for binary value representation
SPILED_REG_LED_LINE 0xffffc104
SPILED_REG_LED_LINE_o 0x0004
bit 25
bit 24
bit 26
bits 15..8
bits 7..0
bits 23..16
bits 31 ...
...0

---
Single Cycle CPU Throughput: IPS = IC / T = IPCstr.fclk
Serial Port – UART
0x00000000 ... 0xefffffff
data
main memory
CPU
RX_ST
.1
.0
0xffffc000
address
receive status
IE
READY
RX_DATA
.7..0
0xffffc004
receive shift register
receive data
TX_ST
.1
.0
0xffffc008
address
decoder
trasmit status
IE
READY
TX_DATA
.7..0
0xffffc00c
transmit shift register

---
QtRVSim Serial Port Addresses
SERIAL_PORT_BASE 0xffffc000
base address of QtRVSim serial port, mirrors on 0xffff0000 for MARS and QtSpim
SERP_RX_ST_REG 0xffffc000 Receiver status register
SERP_RX_ST_REG_o 0x0000 Offset of RX_ST_REG
SERP_RX_ST_REG_READY_m 0x1 Data byte is ready to be read
SERP_RX_ST_REG_IE_m 0x2 Enable Rx ready interrupt
SERP_RX_DATA_REG 0xffffc004 Received data byte in 8 LSB bits
SERP_RX_DATA_REG_o 0x0004 Offset of RX_DATA_REG
SERP_TX_ST_REG 0xffffc008 Transmitter status register
SERP_TX_ST_REG_o 0x0008 Offset of TX_ST_REG
SERP_TX_ST_REG_READY_m 0x1 Transmitter can accept next byte
SERP_TX_ST_REG_IE_m 0x2 Enable Tx ready interrupt
SERP_TX_DATA_REG 0xffffc00c Write word to send 8 LSB bits to terminal
SERP_TX_DATA_REG_o 0x000c Offset of TX_DATA_REG

---
QtRVSim Peripherals Documentation
- All peripherals supported by QtRVSim are described at QtRVSim project page (README.md file)
  https://github.com/cvut/qtrvsim/#peripherals
- The simple 16-bit per pixel (RGB565) framebuffer
  The size corresponds to MZ_APO 480 x 320 pixel display
  components
  - bits 11 .. 15	red
  - bits 5 .. 10	green
  - bits 0 .. 4	blue
  Frame buffer starts at address
  - LCD_FB_START	0xffe00000
  - LCD_FB_END	0xffe4afff

---
It’s only first step
- LinuxDays 2019 – QtMips (https://www.youtube.com/watch?v=fhcdYtpFsyw)
- Student work: CAN/TWAI driver for NuttX (in mainline) and QtRVSim itself
- Peripheries match MZ_APO (Zynq ARM)
- You can meet us at the Embedded World Conference 2022.
  Talk QtRvSim – RISC-V Simulator for Computer Architectures Classes is scheduled June 21, 2022 Session 10.3 – System-on-Chip (SoC) Design RISC-V Development (16:00 - 16:30)